Time Protocol

1. Specification
This project is an implementation of a Time Protocol server, following the RFC 868. It uses the TCP protocol to exchange information with the originating source (via TCP socket).

The server listen on port 37 of its local end-system. When it receives a packet from a client, It retrieves its current local date and time. Then, get the GMT (UTC ±0) date and time which corresponds to that local date and time. Then, the current GMT (UTC ±0) date and time is used to obtain the elapsed seconds since 01 January 1900 00:00 GMT (UTC ±0).

For the response message, the server replies the client with the elapsed seconds as a 32-bits unsigned integer in binary format.

If the server is unable to determine the time at its site or the current GMT (UTC ±0) date and time is before 01 January 1900 00:00 GMT (UTC ±0), It should close the TCP connection without sending anything.

2. Step: Algorithm level

[BEGIN]

1. Etablish a TCP listener on port 37 (via TCP socket).

2. When packet arrives on the process (server) via the TCP socket:
    2-a. Get the current local date and time
(via process Operating System).
    2-b. Get the current GMT (UTC ±0) date and time which corresponds to the current local date and time.
    2-c. Get the elapsed seconds since 01 January 1900 00:00 GMT (UTC ±0) until the current GMT (UTC ±0) date and time (32-bits unsigned integer in binary format).

3. If the time (elapsed seconds) is determined, the process (server) sends it back to the originating source. Otherwise, the process close the TCP connection without sending anything.

[END]